Excerpt of the CEC Final Staff Report, CEC-200-2009-012-SF

CEC has released their final forecast for the next 10 years (it gets revised every 2 years).  The chart below is excerpted from the Final Staff Report, CEC-200-2009-012-SF.  It demonstrates that the forecasted electricity demand for the SDG&E area is lower than CEC had predicted in the 2007 demand forecast.  These forecasts effectively reduce the area demand by 171 MW for the worst-case extreme peak load. The table has the summary of the new forecast, compared to both the 2007 forecast and the June 2009 draft. The top of the table shows total energy consumption, and the lower half shows the peak demand.

CEC used the 1-in-2 extreme temperature forecast for the above summary table. Here is the worksheet that shows the 1-in-10 peak as well.  The 1-in-10 peak for 2010 is also lower than the one in the June draft:  4,963 MW versus 5,134.  Here’s the final worksheet:

| Form 1.5 - SDG&E Planning Area |
| --- |
| Extreme Temperature Peak Demand (MW) |
| Year | 1-in-2 Temperatures | 1-in-5 Temperatures | 1-in-10 Temperatures | 1-in-20 Temperatures | 1-in-5 Multiplier | 1-in-10 Multiplier |
| 2009 | 4,486 | 4,834 | 4,933 | 5,018 | 1.078 | 1.100 |
| 2010 | 4,513 | 4,863 | 4,963 | 5,049 | 1.078 | 1.100 |
| 2011 | 4,572 | 4,927 | 5,028 | 5,115 | 1.078 | 1.100 |
| 2012 | 4,662 | 5,024 | 5,126 | 5,215 | 1.078 | 1.100 |
| 2013 | 4,738 | 5,105 | 5,210 | 5,300 | 1.078 | 1.100 |
| 2014 | 4,791 | 5,163 | 5,268 | 5,360 | 1.078 | 1.100 |
| 2015 | 4,845 | 5,221 | 5,327 | 5,420 | 1.078 | 1.100 |
| 2016 | 4,895 | 5,275 | 5,382 | 5,476 | 1.078 | 1.100 |
| 2017 | 4,954 | 5,338 | 5,447 | 5,541 | 1.078 | 1.100 |
| 2018 | 5,009 | 5,398 | 5,508 | 5,603 | 1.078 | 1.100 |
| 2019 | 5,067 | 5,461 | 5,572 | 5,669 | 1.078 | 1.100 |
| 2020 | 5,126 | 5,524 | 5,637 | 5,735 | 1.078 | 1.100 |