Municipal Regional Permit (draft)

Provision C.3.g. (Treatment Alternative Compliance)

# Text boxes

Regulated Project

Onsite Treatment Impracticable1 and No Regional Project2 Available?

Install Hydraulically-Sized Onsite Treatment in accordance with C.3.d.

Alternative Compliance by Providing Equivalent Offsite Treatment3 in the same watershed

Alternative Compliance by Providing Equivalent Water Quality Benefit8 (e.g., stream restoration)

No

Yes

No

Yes

Minimize New/Replaced Impervious Surface in Site Design and Provide Equivalent Offsite Treatment3 at a Regional Project2

Redevelopment and Brownfield4; Low- or Moderate-Income or Senior Housing5; or Transit Village6?

- Impracticable – Implementation of onsite treatment is considered impracticable under the following criteria:

- Projected cost of treatment measures (labor and materials) exceeds 2% of total project costs;  (Total project cost includes the construction (labor) and materials cost of the physical improvements proposed; but does not include land, transaction, financing, permitting, demolition or offsite mitigation costs) or

- Installation of treatment measures would result in inability of project sponsor to comply with other regulatory requirements at the federal, state and/or local levels.

- Regional Project – A regional or municipal stormwater treatment facility that discharges into the same watershed that the project does.  The Regional Project must be completed within 3 years after the end of construction of the regulated project.

- Equivalent Offsite Treatment – Based on the area of new/replaced impervious surface created by the project, the amount of pollutant loading, surface area, or quantity of runoff, which would be treated if hydraulically-sized treatment controls, in accordance with Provision C.3.d., were installed onsite.  The cost of treatment does not have to exceed 2% of total project costs.

- Brownfield – Use EPA definition but project must receive subsidy or similar benefits under a program designed to redevelop such sites.

- Low-income, moderate-income and senior housing – Use Government Code Section 65589.5(h)(3) or (4) or 65195(b) but for purposes of this section, only the actual low-or moderate-income or senior housing portion of the development will be allowed the “special treatment” provided in this section.

- Transit Village – Developments located within ¼ mile of an existing or planned bus, light rail, heavy rail, or intermodal station and/or major transfer point.  Bus stops are not included in this definition.  An intermodal station or transfer point is where different modes of transportation connect.

- Maximize Site Design Treatment Controls will be defined to include specific measures that must be included in the project, such as bioretention gardens.

- Equivalent Water Quality Benefit will be limited to only certain types of projects (e.g., stream restoration) in the same watershed that will be specifically listed in the permit.

Notes:

- Watershed or the scale of watershed for purposes of C.3.g. will be defined.

- This flowchart represents WB Option for the alternative compliance section.  Individual programs/cities will no longer be able to submit other versions for approval.  This supersedes any alternative compliance programs previously approved by the EO.

Maximize Site Design Treatment Controls7 to provide as much onsite treatment as possible.